## Slide 1
Customized Embedded Processor Design
Sajjad Hussain, Dr. Lars Bauer, Prof. Dr. Jörg Henkel
Laboratory:

## Slide 2: ASIPs: efficiency vs. flexibility
- instruction extension/definition
- parameterization
inclusion/non-inclusion of
functionality/devices
src: Henkel “Design and Architectures for Embedded Systems (ESII)”
Flexibility, 1/time-to-market, …
“efficiency”: MIPS/$, MHz/mW, MIPS/area, …
ASIC:
- Non-programmable,
- highly specialized
General purpose
processor
ASIP
(extensible
processor)
“Hardware solution”
“Software
solution”
The best performance
The highest development cost
Only reasonable for high volume products

## Slide 3: ASIPs: efficiency vs. flexibility
- instruction extension/definition
- parameterization
inclusion/non-inclusion of
functionality/devices
src: Henkel “Design and Architectures for Embedded Systems (ESII)”
Flexibility, 1/time-to-market, …
“efficiency”: MIPS/$, MHz/mW, MIPS/area, …
ASIC:
- Non-programmable,
- highly specialized
General purpose
processor
ASIP
(extensible
processor)
“Hardware solution”
“Software
solution”
Extremely flexible
Bad performance

## Slide 4: ASIPs: efficiency vs. flexibility
- instruction extension/definition
- parameterization
inclusion/non-inclusion of
functionality/devices
src: Henkel “Design and Architectures for Embedded Systems (ESII)”
Flexibility, 1/time-to-market, …
“efficiency”: MIPS/$, MHz/mW, MIPS/area, …
ASIC:
- Non-programmable,
- highly specialized
General purpose
processor
ASIP
(extensible
processor)
“Hardware solution”
“Software
solution”
Optimized for an application
Still flexible, but achieves a better performance

## Slide 5: ASIP Design Flow
Profiling
Implementation
Benchmarking
Test

## Slide 6: Lab Environments
dlxsim: Instruction Set Simulator adapted for our Processor
ASIPMeister: To create new processor and compiler
Extended GCC compiler: compiler out of an processor architecture description in ASIPMeister.
QuestaSim/ModelSim: hardware simulator for RTL Code
Xilinx Vivado/ISE: Synthesis of RTL Code
XPower: To estimate power consumption
Virtex-5 FPGA Evaluation Board
ModelSim Simulation (Signals)
ASIPmeister Software
ASIPMeister Input and Output

## Slide 7: Goal of ASIP Lab
Creating new CPUs with new instructions and implementing these new instructions in Hardware and Software with evaluation and testing
The main goals are:
  creating new ASIPs for special applications
  benchmark those ASIPs to find out their benefits and drawbacks
  and finally to interpret the benchmark results
Lab Structure:
  Weekly Sessions: Eight 2-3 hours sessions per week
  Lab Groups: Group of 2-3 students to carry tasks
  Each group should perform each Week/Session exercises and submit the answers before next session start.

## Slide 8: Pipeline Processor
src: Muhammad Shaaban “The DLX Architecture”, lecture on ‘Computer Architecture’

## Slide 9: Pipelining

## Slide 10: Pipeline Processor Used
Brownie STD 32 is a RISC-type pipeline processor architecture.
The Brownie architecture is designed for an easy and fast pipeline processor.
It is a Load-/Store-architecture,
Parameters | Architecture
Basic architecture | RISC
Memory architecture | Harvard
Instruction length | 32
Data length | 32
Addressing | Byte address
The number of general-purpose registers | 32
The number of pipeline stages | 4
The number of delayed branch slot | 0
Floating-point unit | N/A
Forwarding | full forwarding
Alignment | 1-byte, 2-byte and 4-byte
Endian-ness | Big Endian
Interrupts | Reset, Internal, External

## Slide 11: Profiling on Control-Flow Graph
Blowfish with 1 KB input data: Encrypt and Decrypt
Each node is a Base Block:
  The instructions in a Base Block are always executed together
  No jumps in a Base Block, except the end
  No jump targets in a Base Block, except the beginning

## Slide 12: Constraints for Designing Custom Instructions
Number of Input-/Output-Values to Custom Instruction
  Limited by register file, e.g. 4 read and 2 write ports
‘Forbidden Nodes’, e.g. Load/Store
Convex Graph
Limited Frequency, Area, Power, and/or Energy Budget
  An ASIP that consumes more power may consume less energy, if the application terminates much earlier
load

## Slide 13: Important Documents
Must Read!!!
  Weekly Session Exercise
Optional
  Laboratory Script
  ASIPMeister Users’ Manual (AM_usersmanual_en.pdf)
  ASIPMeister Tutorial (AM_tutorial_en.pdf)
  Brownie STD 32 Reference Manual (BrownieSTD32_Spec_en.pdf)
  Brownie STD 32 Package ReadMe.txt (README_en.txt)
  Using the GNU Compiler Collection (Compiler.pdf)
  The GCC Assembler (GCC Assemble.pdf)
  The GNU linker (linker.pdf)
Following is used as reference material. In each session, only the relevant chapters are asked to read. No need to go through all these.

## Slide 14: Important Directories
/home/asip00/Sessions/SessionX: The lab exercise for each session. For instance; the “Laboratory Script” is placed at Sessions/Session0.
  Before each session is started, the corresponding material will be copied to its folder.
/home/asip00/Documents/: The relevant tutorials and manuals for the Lab.
/home/asip00/epp:
  AM_tools: ASIPmeister tools to generate custom compiler
  ASIPMeisterProjects: a template project
  dlxsimbr_Laboratory: DLXIM simulator to be used
  mkimg: Lab Makefile and Scripts
  StdLib: standard library for I/O

## Slide 15: Important Note
Lab computers, software and hardware can be accessed remotely.
Generally, the sessions need to be executed on one of the following Lab PCs:
i80labpc01, i80labpc02, … i80labpc10
ASIPmeister is ALWAYS executed from i80pc57. This PC can be SSH-ed from any of above PCs i.e. i80labpcXX or from your laptop.
FPGA JTAG driver is setup on i80labpc10, and FPGA board can be accessed via this PC only.
For remote/ONLINE access use ssh –X username@i80labpc10.ira.uka.de

## Slide 16: Important Note
Due to prevailing condition the lab will be conducted ONLINE
Meetings: Though Zoom (mutually decided in Kick-off)
Lab PCs: Accessed through SSH (Using MobaXterm, X2Go, Putty etc.)
User accounts will be sent to you via email

## Slide 17: How to access?
Accessing PC:
  Login to i80labpcXX using user@i80labpcXX.ira.uka.uk via MobaXterm.
  ssh –X user@i80pc57 and perform all exercises here.
  In case you need to implement your application to FPGA, you need to login to i80labpc10, i.e., ssh –X user@ i80labpc10
Accessing Helping Material
  /home/asip00/Documents
  /home/asip00/Sessions
  /home/asip00/epp
Creating recommended directory structure
  Create new project directory for each new project
  Create new application directory for each new application
  To create new project use TEMPLATE_PROJECT.

## Slide 18: Recommended Reading for Session-1
For the first session, read the following:
  ASIPmeister User Manual
  Laboratory Script’s Chapter 1
  Laboratory Script’s Chapter 3 (dlxsim; without 3.2.2, 3.2.3 & 3.3.2)

## Slide 19: An Example: Application
[…]
for ( ; len > 0 ; len-- ) {
/* Step 1 - get the delta value */
if ( bufferstep ) {
delta = inputbuffer & 0xf;
} else {
inputbuffer = *indata++;
delta = (inputbuffer >> 4) & 0xf;
}
bufferstep = !bufferstep;
/* Step 2 - Find new index value (for later) */
index += indexTable[delta];
if ( index < 0 ) index = 0;
if ( index > 88 ) index = 88;
/* Step 3 - Separate sign and magnitude */
sign = delta & 8;
delta = delta & 7;
/* Step 4 - Compute difference and new predicted value */
/*
** Computes 'vpdiff = (delta+0.5)*step/4', but see comment
** in adpcm_coder.
*/
vpdiff = step >> 3;
if ( delta & 4 ) vpdiff += step;
if ( delta & 2 ) vpdiff += step>>1;
if ( delta & 1 ) vpdiff += step>>2;
if ( sign )
valpred -= vpdiff;
else
valpred += vpdiff;
/* Step 5 - clamp output value */
if ( valpred > 32767 )
valpred = 32767;
else if ( valpred < -32768 )
valpred = -32768;
/* Step 6 - Update step value */
step = stepsizeTable[index];
/* Step 7 - Output value */
[…]
#define signedUnsignedModification 0x8000
#if PRINT_ARRAY
t_print(separator);
t_printHex( (valpred+signedUnsignedModification) & 0xFFFF, 4);
if (printCounter%10==9) separator=",\r\n";
else separator=", ";
printCounter++;
#else
if (printCounter&1)
writeToAudioOutL( (valpred+signedUnsignedModification) & 0xFFFF);
else writeToAudioOutR( (valpred+signedUnsignedModification) & 0xFFFF);
printCounter++;
#endif
}
[…]

## Slide 20: An Example: ASIPs
CPU0: The original CPU
CPU1: Optimization for speed
CPU2: Optimization for energy and area

## Slide 21: An Example: Benchmarking
Cycles and Execution Time
CPU Area
Maximal Frequency
Power and Energy Consumption

## Slide 22: An Example: Conclusions
CPU1
Obviously much faster
Only execution speed is here consider.
Optimization Result
CPU2
Less power consumption but slower
Only one resource ALU is used here.
Almost Same Energy Consumption

## Slide 23: An Example: HW Implementation
ASIP Lab Hardware Virtex-5 Setup
Peripheral Board Connections
CPU Signals (ModelSim Simulation)
Output to UART hterm

## Slide 24: Supervisors and the regular meeting
Dr. Lars Bauer
Sajjad Hussain
Regular Meeting: what about Monday 16:00 ?
Questions??